## Slide 1: Infrared alert system with radio frequency capability
T09-Signal senderS
Max Cope
Leslie Eide
Chris Klupenger
SignalSenders

## Slide 2: Problem
Practicum Project Guidelines
SignalSenders
Originated from Sprinklers Systems Designed to Keep Deer off Property
The Systems Lacked Many Features
  Communication Between Units
  Timers
Motivation

## Slide 3: Objective
Develop a Security Network with Communication Capabilities
Utilize Communication within the 2.4GHz ISM band to lessen complexity
Battery Operated to Eliminate Hard Wired Constrictions
SignalSenders

## Slide 4: Alternatives
Wired UNITS
Inefficient at larger ranges
Cables everywhere
Signal Options
WIFI
Bluetooth
RF Signals
IR Signal
SignalSenders

## Slide 5: Requirements
Motion Sensor
Used to sense motion within a specified range
Signal used to send specified signal to microcontroller for further processing
microcontroller
Central to the operation of this system
Takes signal from IR and tells the RF module to send a signal that it detected motion
Takes signal from RF module that another unit sensed motion and light up the corresponding LED associated with the unit ID
Signal
In standby listening for a signal from the other units to send to the microcontroller
When prompted from the Microcontroller a signal with unit ID is transmitted to the other units
SignalSenders

## Slide 6: Approach
SignalSenders
Activity View
Interaction View
Change to something other than interrupt.
Change to 5 pin spi
Change to 1 pin

## Slide 7: Design
Identifying the Appropriate
  Motion Detector
  Microcontroller
  RF Transceiver
  LED Indicators
  Battery Power
  Housing
SignalSenders

## Slide 8: Infrared motion sensor Design
5v Power
Ground
1 Bit Active High Data Bit
User Definable Potentiometers
  Sensitivity
  Rate of (detection?)
SignalSenders

## Slide 9: Radio frequency Communication
Handles All RF Tasks
2.4 GHz ISM Band
  Worldwide license-free
Communication Pipes
  A Unique Pipe for Each Units Communication
  Simultaneous Unit Communication
SignalSenders
SPI interfacing with C
  CE
  CS
  MOSI
  MISO
  SCK
Configurable through Programming
“RF24” Libraries.

## Slide 10: Microcontroller Programming
ATMEGA 328P
Programming
  IR Detect
  RF SPI
  Four LED
  Unit Identification
SignalSenders
Programmed Through SPI

## Slide 11: LED Output
Four LED Outputs
  One LED Indicator to Represent Each Unit
  All Power Sourced from C!
Analog Voltage Signal
Blink to Indicate a Trip on Respective Unit.
  Specified Indication Time Span
SignalSenders

## Slide 12
Verification
Subsections of circuit were built and tested on breadboard
Changes such as digital output pins used, SPI connectivity, etc. stemmed from early verification work

## Slide 13: Implementation Schematic - POWER
SignalSenders

## Slide 14: Implementation Schematic – Modules
SignalSenders

## Slide 15: Implementation PCB
SignalSenders

## Slide 16: Intellectual property prior work
RF Module libraries found online
Open source Arduino coding
Nothing proprietary created
No schematics followed
SignalSenders

## Slide 17: Testing
Strategy
Testing power
Continuity
Layering complexity
Execution
Talk about issues/lack there of
SignalSenders

## Slide 18: Results
4 working units (video potential?)
SignalSenders

## Slide 19: Contributions
Max cope
RF signals
RF Firmware
Leslie Eide
IR motion detector
LED output panel
Chris Klupenger
Microcontroller
Programming
SignalSenders

## Slide 20: Lessons Learned
SignalSenders