## Slide 1: Infrared alert system with radio frequency capability
T09-Signal SENDERS
Max Cope
Leslie Eide
Chris Klupenger
SignalSenders

## Slide 2: Problem
Practicum project guidelines
SignalSenders
Originated from sprinklers systems designed to keep deer off property
Communication between units
Issues with scope of project
Motivation

## Slide 3: Objective
Develop a security network with communication capabilities between units
Utilize communication within the 2.4GHz ISM band to lessen complexity
Battery operated to eliminate hard wired constrictions
Make a visual LED array to confirm motion on each unit with unique ID
SignalSenders

## Slide 4: Alternatives
Wired UNITS
Inefficient at larger areas
Cables everywhere
SINGLE UNITS
One sensor with one receiver
Signal Options
IR Signal
RF Signals
  WI-FI
  Bluetooth
  GFSK 2.4GHz
SignalSenders

## Slide 5: Requirements
MOTION SENSOR
With parameters for range and duration of signal
MICROCONTROLLER
Interface between the IR and RF units
Decode received signal to light corresponding LED
SignalSenders
RF SIGNAL
Ability to send and receive a signal
Range without interference
UNIT IDENTIFICATION
Controllable unique ID
Used within RF signal and LED identification

## Slide 6: Approach
SignalSenders
Activity View
Interaction View

## Slide 7: Design
IDENTIFY
  IR Motion Detector
  RF Transceiver
  Microcontroller
  LED Indicators
  Housing
SignalSenders

## Slide 8: Infrared motion sensor Design
5V Power
Ground
1 Bit Active High Data Bit
Adjustable Parameters
  Sensitivity
  Signal duration
SignalSenders

## Slide 9: Radio frequency Communication
Handles all RF tasks
2.4 GHz ISM Band
  worldwide license-free
Communication Pipes
  A unique pipe for each units communication
  Simultaneous unit communication
SignalSenders
SPI interfacing with μC
  CE
  CS
  MOSI
  MISO
  SCK
Configurable through programming
“RF24” Libraries

## Slide 10: Microcontroller Programming
ATMEGA 328P
Programming
  IR Detect
  RF SPI
  Four LED
  Unit Identification
SignalSenders
Programmed Through SPI

## Slide 11: LED Output
Four LED Outputs
  One LED indicator to represent each unit
  All power sourced from μC!
Analog Voltage signal
5 second LED illuminated to Indicate a trip on respective unit
  Specified indication time span
HOUSING
Self contained unit
Color coordinated for unit identification
SignalSenders

## Slide 12
Initial Verification
Subsections of circuit were built and
  tested on breadboard independently
  Battery power duration
  IR Sensor range and sensitivity
  RF communication
  Microcontroller control
Changes such as digital output pins used, SPI connectivity, etc. stemmed from early verification work

## Slide 13: Implementation Schematic - POWER
SignalSenders

## Slide 14: Implementation Schematic – Modules
SignalSenders

## Slide 15: Implementation PCB
SignalSenders

## Slide 16: Housings
Self Contained Unit
Mounting board/battery/sensor
Visually Identify unit ID

## Slide 17: Intellectual property prior work
RF Module libraries found online
Open source Arduino coding
Nothing proprietary created
No schematics referenced in design
SignalSenders

## Slide 18: Testing
Strategy
Testing power
Continuity
Layering complexity
  combinations
Execution
Battery power/interference
Duration LED output
Errors inconsistent/
  non-repeatable
SignalSenders

## Slide 19: Startup Sequence

## Slide 20: Results
SignalSenders

## Slide 21: Contributions
Max cope
RF signals
RF Firmware
Eagle BOM Verification
Project Design Specifications
Ordering parts/procurement
Building Boards
Leslie Eide
IR motion detector
LED output panel
Housing
Eagle Schematic
Scheduling
System Design and Modeling
Building Boards
Chris Klupenger
Microcontroller
Coding
Eagle board layout
Test plan
Programming boards
Building boards
Testing/troubleshooting
SignalSenders

## Slide 22: Lessons Learned
SignalSenders